## Slide 1: Evac I & II by beacon engineering co., inc.
Aerosol Can Crusher and Recovery System
Machinery designed to help your company
SAVE MONEY and BE GREEN

## Slide 2: EVAC lets you reduce the mass of aerosol cans leaving your plant
RE-DUCE
Cans are crushed in a hermetically sealed Compaction Cylinder for disposal or recycling
B
E
A
C
O
N
N G I N E E R I N G C O.

## Slide 3: EVAC is the Only system with 99.8% recovery efficiency
EVAC II – Up to 2500 cph crushed to wafers for safe disposal or recycling.
RE-USE
EVAC I – Processes 400 to 500 cans per hour
N G I N E E R I N G C O.
B
E
A
C
O
N

## Slide 4
Handling of Contents: Propellant and concentrate are transferred to the primary receiver. Propellant may be drawn off as a gas and compressed into a liquid for use as an alternative fuel source, reused, or incinerated. Concentrate is transferred to standard barrels for transport.
RE-USE
Options for Product Recovery and Recycling
Vacuum System for Safety and Efficiency
Vacuum System: As an additional SAFETY MEASURE, the secondary scavenger function picks up any residual gas left in and around the crushed cans, before releasing them from the crushing cylinder. A piston pump works continuously to hold a vacuum in the tank and delivers the gases to the primary receiver.
B
E
A
C
O
N
N G I N E E R I N G CO.
Vacuum Pump and Tank

## Slide 5: Recycle your steel cans !! Reclaim and Re-use valuable product !! Re-use propellant gases as an alternative fuel
Cans are loaded onto tabletop chain from stainless steel Feed Table, where they are fed into the hermetically sealed Compaction Cylinder. After crushing, the Vacuum System removes any residual contents and vapors. The wafers come up the Drying Conveyor and are deposited into a container for recycling.
RECYCLE
Nickel-Plated Compaction Cylinder
Drying Conveyor area
Feed table & machine operator
Vacuum System
Compaction area

## Slide 6: Control Panel completely air operated Remotely located Hydraulic Power Unit Vacuum System removes residual gases
The Control Panel is by air logic and requires no electricity It is conveniently located for manual or automatic operation, with emergency stop and other safety features. Interlock system ensures proper sequence operation.
SAFETY FEATURES
The Hydraulic Power Unit is to be located just outside the wall or building housing the crushing operation for safety and noise considerations. The Power Unit includes the electric motor, tank heater, heat exchanger and hydraulic pump.

## Slide 7
BEACON ENGINEERING CO.
Designers and manufacturers of quality production machinery for the aerosol industry since 1967.
To view EVAC I in operation, visit our website: www.beaconcan.com , click on machine photo.
E-mail susie@beaconcan.com, or
Phone us @ 706) 692-6411 for DVD or information.
We answer our phone with real people and will be happy to discuss your needs and provide information and quotations.